## Slide 1: Smart Eye Glass with Face recognition and obstacle Detection for Virtually impaired
Group no. 1
19BCS014 Md Minhaaz
19BCS031 Shahabuddin

## Slide 2: Objectives
Introduction
Block Diagram
Working
Obstacle Detection
Face Recognition
Limitations
References

## Slide 3: Introduction
There are approx. 2.2 billion people who are visually impaired or blind, according to 2022 World Health Organization (WHO) research on disability.
Our aim is to create a small eye glass that will be able to detect face and recognize people.
It can also detect obstacles and calculate distance to alert the user.
Normal Eye Glass
Smart Eye Glass
Face Recognition
Obstacle Detection

## Slide 4: Block Diagram
Raspberry Pi3
Ultrasonic
Sensor
Camera
Power
Supply
Earphone or
Speaker

## Slide 5: Working
Smart Eye Glass
Check if it’s a human or not
Run facial recognition model
Calculate distance
Alert the user using voice
If obstacle is detected
If human
If not
Repeat

## Slide 6: Obstacle Detection
Ultrasonic Sensor
Working Principle
Distance Calculation
Raspberry Pi pin
Connection

## Slide 7
Ultrasonic Sensor && Working Principle
Here, time taken = transmitter to object +
object to receiver
Thus, we need to consider half of the time taken
(time taken/2) to calculate distance.
Finally, distance = speed of sound x (time taken/2)
The HC-SR04 Ultrasonic sensor has four pins.
Vcc
TRIG (input)
ECHO (output)
GND

## Slide 8
Distance Calculation
Set the trig pin high for some time(3 to 100 us)
As soon as trig pin is low, the sensor send pulses and set echo pin to high
When the sensor gets the reflected pulses, it set the echo pin to low.
We need to measure time for which echo pin was high.
Speed of Sound = 343 m/sec = 34300 cm/sec
Distance Detected = (speed * time) / 2
= (34300 * time) / 2
= 17150 * time
Distance Detected = (17150 * time ) cm/sec
Here,
time = Time duration when echo pin is high
= echo_pulse_end – echo_pulse_start

## Slide 9
Raspberry Pi pin
GPIO (General Purpose Input Output)
5v PWR
3.3v PWR
Reserved
GND
It has 40 pins

## Slide 10
Ultrasonic Sensor with Raspberry Pi3
Connection
Trig  21 GPIO pin (40th pin)
Echo  20 GPIO pin (38th pin)
VCC  5V PWR pin ( 4th pin)
GND  GND pin (6th pin)

## Slide 11: Face Recognition
Connection
Overall Connection
The Smart Eye Glass

## Slide 12
Camera with Raspberry Pi3
Connection

## Slide 13: Overall Connection
Finally, the sensor HC-SR04 and the camera are connected to Raspberry Pi3

## Slide 14: The Smart Eye Glass

## Slide 15: Limitations
In the Following 4 cases:
Object is too far away
Flat object is not facing sensor
Object is too small
Object is too soft
Case i
Case ii
Case iii
Case iv

## Slide 16: References
[1] https://www.who.int/news-room/fact-sheets/detail/blindness-andvisualimpairment#:~:text=Globally%2C%20at%20least%202.2%20billi on,near%20or%20distance%20vision%20impairment.
[2] Ultrasonic Smart Spectacles for Visually Impaired and Blind People
Authors: L. Shashitha (Department of Electronics and Communication Engineering, Institute of Aeronatical Engineering College Dundigal, Hyderabad, Telangana) P. Ashok Babu (Department of Electronics and Communication Engineering, Institute of Aeronatical Engineering College Dundigal, Hyderabad, Telangana)
Published in: 2021 3rd International Conference on Advances in Computing, Communication Control and Networking (ICAC3N)
Date of Conference: 17-18 December 2021 Date Added to IEEE Xplore: 09 March 2022 Electronic
ISBN:978-1-6654-3811-7 Print on Demand(PoD)
ISBN:978-1-6654-3812-4
INSPEC Accession Number: 21666268
DOI: 10.1109/ICAC3N53548.2021.9725747
Publisher: IEEE Conference
Location: Greater Noida, India

## Slide 17: Any….
Suggestions…??
From your side…..

## Slide 18: Thank You….